## Slide 1: Phantom: Exploiting Decoder-detectable Mispredictions By: Johannes Wikner, Daniël Trujillo and Kaveh Razavi
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
January 31, 2025

## Slide 2: Background
The Branch Prediction Unit (BPU) provides a prediction of the upcoming control flow by:
  Storing recent control-flows in Branch History Buffers (BHBs)
  Holding predictions, indexed by BHBs, in Branch Target Buffers (BTBs)
BPU
IF
ID
EX
Retire
Time

## Slide 3: Branch Prediction
Mispredicted instructions are processed in the pipeline until a resteer signal is provided – known as the speculation window
  This is the mechanism exploited by Spectre
BPU
IF
ID
EX
Retire
Mispredicted Target
Resteer
Speculation Window

## Slide 4: Spectre
Abuses speculative execution to perform mispredicted operations and leak victim’s information via side-channels
  Circumvents numerous security countermeasures
Phantom proposes a new Spectre class that considers shorter speculation windows
  Resteer is issued before instruction reaches execute stage

## Slide 5: Phantom
Cases where training and victim branch sources are different are commonly considered non-exploitable
  Instruction mismatches can be discovered at decode and resteered before execution
  Previously believed to result in too short of a speculation window
Asymmetric cases have been proven to also lead to long speculation windows
Phantom provides a methodology for user-to-kernel exploitation on shorter speculation windows

## Slide 6: Phantom Contributions
Provides tools for measuring transient fetch and decode of mispredicted targets
Analysis of mispredictions and how far instructions get in the pipeline
Presents the Phantom class of attacks
Proves ability to break KASLR and leak arbitrary kernel memory

## Slide 7: Observing Mispredictions
Instruction Fetch (IF): Measure the I-cache state using a timing side-channel
  Not effective for distinguishing IF from BPU-assisted I-cache prefetching
Instruction Decode (ID): Samples performance counters indicating µop-cache use
  Less reliable on Intel architectures than on AMD
Execute (EX): Detects execution by using a single memory fetch in the mispredicted path
  Due to shorter speculation, resteer is issued before memory operations can be performed
Table 2, Pg. 6

## Slide 8: Branch Mispredictions
Phantom uses a training and victim branch to cause mispredictions
  Study of instruction combinations causing mispredictions
  How far in the pipeline mispredictions get before a resteer
Table 1, Pg. 6

## Slide 9: Phantom
Phantom speculation attacks are broken down into three steps:
  Train the BTB to a target
  Execute the victim
  Infer whether the target was loaded from memory (can use Prime+Probe)
Figure 5, Pg. 5
Figure 4, Pg. 5

## Slide 10: Phantom Attack Primitives
Detecting mapped executable memory
    Fetch only populated I-cache if executable and backed by physical memory
Non-mapped executable memory
    Failed fetch leaves I-cache unaffected
    Adversary can trigger a data load
    Requires a disclosure gadget
Leaking register values
    Filters a single byte from the register and aligns with the cache-line
    Creates an offset into victim’s address space and loads resulting address
(AMD Zen 1 & 2 only)

## Slide 11: Kernel Address Collision
text

## Slide 12: Breaking KASLR
text

## Slide 13: Mitigation
text

## Slide 14: Conclusions
text

## Slide 15: Strengths
Digestible
Relevant (affects billions of users)
Methodology is affective

## Slide 16: Weaknesses
Very little proposed solution
Could provide more well-rounded information on how some structures work or their impact
Presentation of results is somewhat confusing (time to decode)

## Slide 17: Thoughts
text?

## Slide 18: Sources
[1] Akshaye Senoi, Prasanna Karthik Vairam, Kanav Sabharwal, Jialin Li and Dinil Mon Divakaran (2023) iPET: Privacy Enhancing Traffic Perturbations for Secure IoT Communications. In: Proceedings on Privacy Enhancing Technologies.