## Slide 1
[1] Dayeol Lee, David Kohlbrenner, Shweta Shinde, Krste Asanovic, and Dawn Song, Keystone: An Open Framework for Architecting Trusted Execution Environments, In Fifteenth European Conference on Computer Systems (EuroSys ’20) 2020.
[2] Jason Lowe-Power, Abdul Mutaal Ahmad, Ayaz Akram, Mohammad Alian, and et. Al, The gem5 Simulator: Version 20.0+, 2007.
[3] Zach Moolman and Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory, In: Eighth Workshop on Computer Architecture Research with RISC-V (CARRV 2024)
In order to further protect state-of-the-art TEEs, Keystone is extended to include secure memory protocols in the gem5 simulation environment
Trusted Execution Environments (TEEs) provide hardware guarantees that seek to protect the security and isolation of off-chip data.
This work outlines methods for implementing and evaluating contributions to open-source TEEs within architectural simulation.
Extending Trusted Execution Environments in Architectural Simulators
Will Buziak Iris Bahar Tamara Silbergleit Lehman Zach Moolman
Many TEE implementations exist, but Keystone [1] is a popular, open-source version with many pre-existing simulator components.
Keystone provides security through memory isolation, utilizing customized RISC-V hardware primitives.
For Researchers to continue developing secure hardware [3] using Keystone components, contributions must then implement hardware designs and corrresponding ISA extensions.
Gem5 [2] presents architectural design from the bottom-up with ISA protocols, hardware descriptions and user-space benchmarking, enabling full-stack development.
In order to build Keystone in gem5, the developer must also make use of full-system resources.
This work proposes ready-built simulations, reducing set-up time for future developers to implement their contributions.
Potentially Malicious
Application Thread
Operating System
Remote or Cloud User
Main Memory
TEE
Keystone
Background
Simulation allows a shorter pipeline from design idea to implementation testing.
Achieving a baseline model is non-trivial, requiring extensive knowledge of the simulator itself.
Development Time
Fabrication
FPGA
Simulation
Untrusted
App
App
Operating System
(OS)
Enclave 1
Enclave App 1 (Eapp)
Runtime (RT) 1
Enclave 2
Eapp 2
RT 2
Security Monitor
Trusted Hardware
RISC-V Cores
Optional H/W Features
Root of Trust
Tools for Extension
User
(U-Mode)
Supervisor
(S-Mode)
Machine
(M-Mode)
Keystone
SGX
TrustZone
...
Phantom
...
Proprietary
Open-Source
TEEs
Ready-Made Simulation
Goals
Memory Isolation
PMP Table
Root of Trust
Runtime
Remote Attestation
Encryption/ Integrity
ISA Primitives
Microarchitecture Designs
Future Work
gem5
Motivation
Bibliography
cpp Implementation
Python Wrapper
Hardware Description
Config Files
User Space
Program Binary
Boot-loader
gem5 Pre-compiled Resources
Linux Kernel
Disk Image
Security Monitor
Department of Computer Science Department of Computer Science Department of Electrical, Computer, & Energy Department of Electrical, Computer, & Energy
Engineering Engineering
Bench-marking
Implement Designs
Existing Implementations
Memory Encryption Engine
Port Connections
New Components