## Slide 1: Secure Extensions for RISC-V Trusted Execution Environments
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
April 24, 2025

## Slide 2: Motivation
Goal: Provide efficient secure memory extensions for TEEs and a methodology for developing TEEs in simulation
State-of-the-art Trusted Execution Environments support secure memory protocols, but often do not use these methods due to lots of overhead
Researching TEEs requires baseline expertise in the development medium, typically:
  FPGA
or
  Simulation

## Slide 3: Brief Introduction to Trusted Execution
Keystone
SGX
TrustZone
...
Phantom
...
Proprietary
Open-Source
TEEs
Trusted Execution Environments (TEEs) protect memory through hardware guarantees:
  Memory isolation
  Permission assignment
  Root of trust & remote attestation
There are numerous “flavors” of TEE, produced both in academia and industry

## Slide 4: Brief Introduction to Trusted Execution
Keystone
SGX
TrustZone
...
Phantom
...
Proprietary
Open-Source
TEEs
Trusted Execution Environments (TEEs) protect memory through hardware guarantees:
  Memory isolation
  Permission assignment
  Root of trust & remote attestation
There are numerous “flavors” of TEE, produced both in academia and industry

## Slide 5: RISC-V Keystone
Keystone is a popular, open-source TEE, protecting against a malicious:
Operating system
User thread
Cloud or remote user
This is achieved by breaking down memory regions into three permissions, or modes
Untrusted
App
App
OS
Enclave 1
Runtime (RT) 1
Enclave 2
Eapp 2
RT 2
Security Monitor
Trusted Hardware
RISC-V Cores
Optional H/W Features
Root of Trust
Extension Framework
User
(U-Mode)
Supervisor
(S-Mode)
Machine (M-Mode)
Enclave App 1 (Eapp)
Untrusted
App
OS
Enclave 1
Runtime
Security Monitor
Trusted Hardware
RISC-V Cores
Optional H/W Features
Root of Trust
Extension Targets
User
(U-Mode)
Supervisor
(S-Mode)
Machine (M-Mode)
Eapp 1
App
App
Enclave 2
RT 2
Eapp 2
Dayeol Lee, David Kohlbrenner, Shweta Shinde, Krste Asanovic, and Dawn Song, Keystone: An Open Framework for Architecting Trusted Execution Environments, EuroSys 2020.

## Slide 6: Keystone Limitations
Currently, Keystone only protects storage due to latency and memory overhead, our work focuses on addressing these concerns by:
Fortification of Keystone hardware with efficient secure memory methods to protect against off-chip corruption:
Implementing a hardware / software co-design, providing:
  Modified / Extended Keystone hardware components
  Performance improvements on Keystone security processes

## Slide 7: Where does Secure Memory fit in?
Secure Memory
RISC-V Keystone
Application Thread
Operating System
Remote or Cloud User
Potentially Malicious
Storage
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
Secure memory methods protect SoCs against off-chip memory corruption by additionally:
  Encrypting / Decrypting protected memory
  Storing and checking an integrity tree to verify data
These checks result in latencies both in encryption and memory

## Slide 8: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 9: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 10: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 11: Keystone Memory Isolation
On boot, the Security Monitor (SM) sets up a component called the Physical Memory Protections (PMP) Table:
Divides memory and assigns to modes
Resides in each core
If a memory request from an application does not have access, it is denied
RISC-V Keystone
Application Thread
Operating System
Remote or Cloud User
Potentially Malicious
Dayeol Lee, David Kohlbrenner, Shweta Shinde, Krste Asanovic, and Dawn Song, Keystone: An Open Framework for Architecting Trusted Execution Environments, EuroSys 2020.
PMP
DRAM

## Slide 12: Extending Keystone to include Efficient Secure Memory
To mitigate latency concerns, our work proposes to store metadata on-chip, greatly reducing memory access overhead
This structure is called the Aggregated Extended PMP (ePMP) table:
Tracks requests through the Memory Encryption Engine (MEE)
Updates metadata entries corresponding to their PMP status
DRAM
Zach Moolman & Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory CARRV 2024
Memory Encryption Engine
ePMP
RISC-V Keystone

## Slide 13: Extending Keystone to include Efficient Secure Memory
To mitigate latency concerns, our work proposes to store metadata on-chip, greatly reducing memory access overhead
This structure is called the Aggregated Extended PMP (ePMP) table:
Tracks requests through the Memory Encryption Engine (MEE)
Updates metadata entries corresponding to their PMP status
DRAM
Zach Moolman & Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory CARRV 2024
Memory Encryption Engine
ePMP
RISC-V Keystone
CPU
SoC

## Slide 14: The gem5 Simulation Suite
gem5 is an open-source, cycle-accurate architecture emulation platform
Allows end-to-end development including full-system simulation & benchmarks
Breaks hardware description into different layers, enabling researchers to edit any aspect of an implementation
This is helpful, but also results in a colossal codebase
Jason Lowe-Power, Abdul Mutaal Ahmad, Ayaz Akram, Mohammad Alian, et al. (2007), The gem5 Simulator: Version 20.0+ (arXiv)
cpp Implementation
Python Wrapper
Hardware Description
Config Files
User Space
Program Binary

## Slide 15: Challenges with gem5
Linux Kernel
Disk Image
gem5 Pre-compiled Resources
Boot-loader
This work requires the use of gem5 full-system emulation, while many aspects of gem5 enable research, some also hinder progress
  Scattered source files
  Lots of detail, making high-level understanding non-trivial
  FS requires gem5 resources and pre-compiled binaries

## Slide 16: Direction / Future Work
Further extending Keystone in gem5, emphasizing:
  User Configurability
  Performance-Security tradeoff
Simulation Tools:
  How can we improve the learning curve to enable new researchers to contribute to TEEs?
Design Idea
&
Implement
Test
Learn gem5
Learn Keystone

## Slide 17: Direction / Future Work
Further extending Keystone in gem5, emphasizing:
  User Configurability
  Performance-Security tradeoff
Simulation Tools:
  How can we improve the learning curve to enable new researchers to contribute to TEEs?
Design Idea
Implement
Test
Learn Keystone
Learn gem5

## Slide 18: Additional Sources
Brian Rogers & Milos Prvulovic (2007) Using address independent seed encryption and bonsai merkle trees to make secure processors OS-and performance-friendly. In: 40th IEEE/ACM International Symposium on Microarchitecture (MICRO’07)
Ayaz Akram et al. darchr/Keystone-experiments. 2021. url: https://github.com/
darchr/Keystone-experiments.
Gueron, S. (n.d.). A Memory Encryption Engine Suitable for General Purpose Processors.
Thomas, S., Workneh, K., McCarty, J., Izraelevitz, J., Lehman, T., & Bahar, R. I. (2024). A Midsummer Night’s Tree: Efficient and High Performance Secure SCM. International Conference on Architectural Support for Programming Languages and Operating Systems – ASPLOS

## Slide 19: Collaborators
Dr. Iris Bahar
Department of Computer Science
Colorado School of Mines
Dr. Samuel Thomas
Department of Computer Science
Brown University
Pomona College
Dr. Tamara Silbergleit Lehman
Department of Electrical, Computer & Energy Engineering
University of Colorado, Boulder
Zach Moolman
Department of Electrical, Computer & Energy Engineering
University of Colorado, Boulder