## Slide 1
Designs in simulation can be tested on real workloads and state-of-the-art, or custom benchmarks.
In order to further protect state-of-the-art TEEs, Keystone is extended to include secure memory protocols in the gem5 simulation environment
Trusted Execution Environments (TEEs) provide hardware guarantees that seek to protect the security and isolation of application data.
This work outlines methods for implementing and evaluating contributions to open-source TEEs within architectural simulation.
Extending Trusted Execution Environments in Architectural Simulators
Will Buziak Iris Bahar
Department of Computer Science Department of Computer Science
Many TEE implementations exist, but Keystone is a popular, open-source version with many pre-existing simulator implementations.
Keystone achieves isolation by segmenting memory & defining rules for different threads with a structure called a PMP table.
This work proposes ready-made simulations, reducing set-up time for future developers to build their contributions.
gem5 presents architectural design as typical class structures with attributes based on the behavior of the real world component
For example, to properly connect the PMP to the proposed ePMP, it is either necessary to write a new:
- Packet type, bypassing the cache hierarchy
Or
- Port type directly connecting the core(s) to the Memory Encryption Engine
Developers wishing to extend Keystone components can create their own version of the desired component’s class structure, often requiring close attention to:
- Port connections
- Packet handling
Real-world Benchmarking
Potentially Malicious
Application Thread
Operating System
Remote or Cloud User
Main Memory
TEE
Keystone
Workflow
gem5
Insights
Background
Experimentation within simulation allows a shorter pipeline from design idea to implementation testing.
Achieving a baseline model is non-trivial, requiring extensive knowledge of the simulator itself.
Development Time
Fabrication
FPGA
Simulation
Untrusted
App
App
Operating System
(OS)
Enclave 1
Enclave App 1 (Eapp)
Runtime (RT) 1
Enclave 2
Eapp 2
RT 2
Security Monitor
Trusted Hardware
RISC-V Cores
Optional H/W Features
Root of Trust
Tools for Extension
User
(U-Mode)
Supervisor
(S-Mode)
Machine
(M-Mode)
Keystone
SGX
TrustZone
...
Phantom
...
Proprietary
Open-Source
TEEs
Implement Designs
Ready-Made Simulation
Goals
Motivation