## Slide 1: Secure Extensions for RISC-V Trusted Execution Environments
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
May 9, 2025

## Slide 2: Motivation
Goal: Provide security to tera-scale memory storage
Trusted Execution Environments support secure memory methods, but often do not employ them due to costly memory overhead:
  Merkle tree memory accesses increase with protected memory size’
Many enclaves that do provide integrity either only support small amounts of memory, or completely abandon ‘freshness’
  No support for large-scale memory storage
  Open to replay attacks

## Slide 3: Secure Memory Incurs Latency
Secure Memory
TEE
Main Memory
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
Monotonically incrementing counters are stored in a merkle tree to prevent replay attacks
  Integrity checks trigger otherwise unnecessary memory fetches
  Counters are incremented on every write
On a memory fetch, the core must do an additional:
  7 memory accesses per read/write for a 128 MB Cache & 8-ary tree
  Cache hit rate suffers as the tree grows
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 4: CXL and Smart Memory
CXL Integrity Data Encryption provides secure connections between trusted components
  Ensure confidentiality, integrity and replay protection
Uses non-deterministic AES stream ciphers and MAC checks
  Enables low latency and bandwidth overhead
  Does not wait for integrity checks before processing data

## Slide 5: Trusted Smart Memory
Stacked DRAM sits on a logic layer
  Connected by Through-silicon-vias
  Can offer up to 168GB of space
Can be utilized to expand trusted computing base
  Builds a secure channel between processor and smart memory
  Eliminates need for ‘freshness’
Trusted Compute Layer
16 layers of 32 GB DRAM

## Slide 6: Trusted Smart Memory
Compute-capable memory
  Mitigates side-channels
  More expensive
Ensures that any tampering or observation will destroy the functionality of the device
  Negates the need for a merkle tree
Not feasible to replace an entire memory rack (up to 28TB)
Trusted Compute Layer
16 layers of 32 GB DRAM

## Slide 7: Toleo
To avoid the costs of storing everything in smart memory
  Only stores ‘versions’ (counters)
  Still utilizes a scheme to increment counters
  Negates the need for a merkle tree
Employs a compression format that limits metadata storage while maintaining coverage at scale
  Kept in smart memory
  Stores data and MAC tags in conventional memory

## Slide 8: Version storage
CXL uses a non-deterministic stream cipher, so identical communication is represented as unique ciphers
  Allows for secure transmission of versions to processor
  Low latency and bandwidth
Employs a compression format that limits metadata storage while maintaining coverage at scale
  Only keeps lower 27-bits (“stealth version”), rest goes to conventional memory
  Compresses the stealth version
Presents stealth version cache
  Boasts a 98% hit rate, reducing memory bandwidth and latency

## Slide 9: Refresh
Versions are confidential from end-to-end
  Replay attacks are reduced to random guessing
  Adversaries only have one chance, otherwise the system will enact a “kill-switch”
Toleo initializes versions to a random value between 0 - 227
  If initialized to a known value and increases monotonically, an attacker can infer its value by the addresses
  Monotonically increases with rollover
  Must be reset before the “lapping” to the initial value
On each counter increment, there is a 1 in 220 chance for a refresh
  Incredibly unlikely to loop back without a reset (1.7 x 10-19)

## Slide 10: Refresh
On a reset, the upper version (portion sent to main memory) is incremented
  Therefore, even though the “stealth version” may repeat at some point, the combined version will remain unique
  Guaranteed to be non-repeating and therefore protected against memory traffic analysis attacks

## Slide 11: Strengths
Dwarfs competition in protected coverage at very little added latency
Employs a compression format that limits metadata storage while maintaining coverage at scale
  Stores data and MAC tags in conventional memory

## Slide 12: Weaknesses
If an integrity check fails, it triggers a kill-switch that destroys the enclaves and all the sensitive data before shutting down