## Slide 1: SecuriTEE: Secure Memory for RISC-V Trusted Execution Environments
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
November 5, 2024

## Slide 2: Background
Motivated attackers can employ many tactics to corrupt or steal data, this work focuses on preventing:
  A malicious OS, application or thread
  Replay or side-channel attacks targeting off-chip peripherals
Trusted Execution Environments (TEEs) provide hardware guarantees that separate address spaces, securing the integrity of the processor
Secure Memory methods protect against off-chip tampering by encrypting and storing metadata securely on-chip

## Slide 3: Motivation
Goal: Harden TEEs with Secure Memory protocols to further protect data integrity
TEEs provide confidence against malicious applications attempting to tamper with data
  Still vulnerable to side-channel attacks, replay attacks and off-chip tampering
Secure Memory can mitigate these concerns by adding another layer of protection for off-chip devices
RISC-V TEEs (e. g. Keystone[1]) provides an open-source, configurable platform for developing TEEs to specific applications

## Slide 4: Trusted Execution Environments
A TEE implements different privelege modes with separate address spaces, enforcing a set of rules dictating which components can access what regions of memory:
  User mode, Supervisor mode, Machine mode
Almost all major CPU vendors have their own flavor of TEE:
  Intel SGX
  ARM Confidential Computer Architecture
  AMD SEV
These implementations leverage proprietary hardware, opening the door for a configurable & open-source TEE, keystone[1]
  Still vulnerable to side-channel & replay attacks

## Slide 5: Secure Memory
Secure Memory defines any off-chip device as untrusted & defines a process for verifying the integrity of off-chip data
Off-chip data is signed with a counter, cryptographically hashed and stored in a tree of hashes (merkle tree[2] & bonsai merkle tree[3])
  Optimizations have been investigated that reduce memory overhead and efficient incrementing of counters
Builds a hash tree over the memory, the root of which is always stored on-chip
  Memory blocks are fetched, hashed and compared against the entire tree for verification

## Slide 6: gem5
gem5 is one of, if not the only, architecture simulator that supports RISC-V & multi-core simulation
  Keystone including PMP tables & checker implementations
  Memory encryption engine
  Secure Memory implementation (Sam Thomas)

## Slide 7: gem5 Simple Sanity Check
Base gem5 vs. Secure Memory implementation (version 24.0.0.1)
  Benchmark:
  10,000,000 accesses on 1GB array of memory
Secure memory implementation requires an increase in both runtime and memory overhead
 | Simulated Time (Seconds) | Host Memory (MB) | Number of Instructions (millions)
Base gem5 |  |  | 
Secure gem5 | 61.9 | 3.44 | 245.989

## Slide 8: gem5 Simple Sanity Check
Base gem5
Secure gem5
hello world
array-flip
hello world
array-flip
Simulated Time (seconds)
Host Memory (MB)
Number of Instructions
.001425
3.4
5892
61.9
3.44
254.989
Binary

## Slide 9: Direction / Future Work
Implementing Zach’s Design:
  Currently adding cache hierarchy
  How to have two separate processors in gem5?
  “Implement then Optimize”
What is my contribution?
  Until now, I have been just trying to implement Zach’s work in gem5
  Deeper understanding of attack methods (winter break project?)
Moolman, Z. & Lehman T.

## Slide 10: Gap & Contribution
A Midsummer Nights Tree (AMNT) by Sam Thomas
  Crash consistent secure memory protocol

## Slide 11: Limitations
Computational and memory overhead

## Slide 12: Sources
[1] Dayeol Lee (2022) Building Trusted Execution Environments. In: A dissertation submitted in partial satisfaction of the requirements for the degree of Doctor of Philosophy in Computer Science in the Graduate Division of the University of California, Berkeley.
[2] Chenyu Yan, Brian Rogers, Daniel Englender, et. al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. In: Proceedings of the 33rd International Symposium on Computer Architecture (ISCA’06)
[3] Brian Rogers & Milos Prvulovic (2007) Using address independent seed encryption and bonsai merkle trees to make secure processors OS-and performance-friendly. In: 40th IEEE/ACM International Symposium on Microarchitecture (MICRO’07)
[3] Zach Moolman & Tamara Silbergleit Lehman (2024) Extending RISC-V Keystone to Include Efficient Secure Memory