## Slide 1
[1] Dayeol Lee, David Kohlbrenner, Shweta Shinde, Krste Asanovic, and Dawn Song, Keystone: An Open Framework for Architecting Trusted Execution Environments, In Fifteenth European Conference on Computer Systems (EuroSys ’20) 2020.
[2] Jason Lowe-Power, Abdul Mutaal Ahmad, Ayaz Akram, Mohammad Alian, and et. Al, The gem5 Simulator: Version 20.0+, (arXiv) 2007.
[3] Zach Moolman and Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory, In: Eighth Workshop on Computer Architecture Research with RISC-V (CARRV 2024)
RISC-V Keystone
This work proposes a framework that aims to assist future developers to implement their contributions.
Our goal is to provide researchers with tools that expedite the development cycle when working with TEEs, primarily targeting:
  New researcher learning curve
  Novel contribution development time
  Testing methods
Trusted Execution Environments (TEEs) provide hardware guarantees that seek to protect the security and isolation of off-chip data.
This work outlines methods for implementing and evaluating contributions to open-source TEEs within architectural simulation.
Extending Trusted Execution Environments in Architectural Simulators
Will Buziak Iris Bahar Tamara Silbergleit Lehman Zach Moolman
Many TEE implementations exist, but Keystone[1] is a popular, open-source version with many pre-existing simulator components.
Keystone provides security through memory isolation, utilizing customized RISC-V hardware primitives.
For researchers wishing to continue developing Keystone components, contributions must also implement hardware designs, built on corrresponding ISA extensions.
Gem5[2] presents architectural design from the bottom-up with ISA protocols, hardware descriptions and user-space benchmarking, enabling full-stack development.
In order to build Keystone in gem5, the developer must also make use of full-system resources.
In order to further protect state-of-the-art TEEs, we extend[3] Keystone to include secure memory protocols in the gem5 simulation environment.
Potentially Malicious
Application Thread
Operating System
Remote or Cloud User
Main Memory
TEE
Keystone
Background
Simulation allows a shorter pipeline from design idea to implementation testing.
Achieving a baseline model is non-trivial, often allocating much of the development time to de-coupled, self-guided learning.
Development Time
ASIC
FPGA
CPU
Untrusted
App
App
Operating System
(OS)
Enclave 1
Enclave App 1 (Eapp)
Runtime (RT) 1
Enclave 2
Eapp 2
RT 2
Security Monitor
Trusted Hardware
RISC-V Cores
Optional H/W Features
Root of Trust
Extension Framework
User
(U-Mode)
Supervisor
(S-Mode)
Machine
(M-Mode)
Keystone
SGX
TrustZone
...
Phantom
...
Proprietary
Open-Source
TEEs
Memory Isolation
PMP Table
Root of Trust
Runtime
Remote Attestation
Encryption/ Integrity
ISA Primitives
Microarchitecture Designs
Future Work
gem5
Motivation
Bibliography
cpp Implementation
Python Wrapper
Hardware Description
Config Files
User Space
Program Binary
Boot-loader
gem5 Pre-compiled Resources
Linux Kernel
Disk Image
Security Monitor
Department of Computer Science Department of Computer Science Department of Electrical, Computer, & Energy Department of Electrical, Computer, & Energy
Engineering Engineering
Bench-marking
Existing Implementations
Memory Encryption Engine
Port Connections
New Components
Potentially Malicious
Application Thread
Operating System
Remote or Cloud User
Secure Memory
RISC-V Keystone
Novel Ideas
Full-System Simulation
Implement Designs
Design Idea
&
Implement
Test
Learn gem5
Learn Keystone
Design Idea
Implement
Test
Learn Keystone
Learn gem5