## Slide 1: Phantom: Exploiting Decoder-detectable Mispredictions By: Johannes Wikner, Daniël Trujillo and Kaveh Razavi
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
January 31, 2025

## Slide 2: Background
The Branch Prediction Unit (BPU) provides a prediction of the upcoming control flow when the pipeline is dependent on the result of currently executing instructions
  Branch History Buffers (BHBs) contain recent control-flows
  Branch Target Buffers (BTBs) hold predictions and are indexed by BHBs
BPU
IF
ID
EX
Retire
Time

## Slide 3: Branch Prediction
Mispredicted instructions are processed in the pipeline until a resteer signal is provided – known as the speculation window
  This is the mechanism exploited by Spectre
BPU
IF
ID
EX
Retire
Mispredicted Target
Resteer
Speculation Window

## Slide 4: Spectre
Takes advantage of speculative execution to perform mispredicted operations and leak victim’s information via side-channels
  Circumvents numerous security countermeasures
Phantom proposes a new Spectre class that considers shorter speculation windows
  Resteer is issued before instruction reaches execute stage

## Slide 5: Phantom
Cases where training and victim branch sources are different are commonly considered non-exploitable
  Instruction mismatches can be discovered at decode and resteered before execution
  Previously believed to result in a short speculation window
Recently proven that these asymmetric cases can also lead to long speculation windows
Phantom analyzes mispredictions and provides a methodology for user-to-kernel exploitation on shorter speculation windows

## Slide 6: Phantom Contributions
Provides tools for measuring transient fetch and decode of mispredicted targets
Analysis of mispredictions and how far instructions get in the pipeline
Presents the Phantom class of attacks
Proves ability to break KASLR and leak arbitrary kernel memory

## Slide 7: Observing Mispredictions
Instruction Fetch (IF): Measure the I-cache state using a timing side-channel
  Not effective for distinguishing IF from BPU-assisted I-cache prefetching
Instruction Decode (ID): Samples performance counters indicating µop-cache use
  Less reliable on Intel architectures than on AMD
Execute (EX): Detects execution by using a single memory fetch in the mispredicted path
  Due to shorter speculation, resteer is issued before memory operations can be performed
Table 2, Pg. 6

## Slide 8: Branch Mispredictions
Phantom uses a training and victim branch to cause mispredictions
  Study of instruction combinations causing mispredictions
  How far in the pipeline mispredictions get before a resteer
Table 1, Pg. 6

## Slide 9: Phantom
Phantom speculation attacks are broken down into three steps:
  Train the BTB to a target
  Execute the victim
  Infer whether the target was loaded from memory (can use Prime+Probe)
Figure 5, Pg. 5
Figure 4, Pg. 5

## Slide 10: Phantom Attack Primitives
text

## Slide 11: Breaking KASLR
text

## Slide 12: Mitigation
text

## Slide 13: Conclusions
text

## Slide 14: Strengths
Digestible
Relevant (affects billions of users)
Methodology is affective

## Slide 15: Weaknesses
Very little proposed solution
Could provide more well-rounded information on how some structures work or their impact
Presentation of results is somewhat confusing

## Slide 16: Thoughts
text?

## Slide 17: Sources
[1] Akshaye Senoi, Prasanna Karthik Vairam, Kanav Sabharwal, Jialin Li and Dinil Mon Divakaran (2023) iPET: Privacy Enhancing Traffic Perturbations for Secure IoT Communications. In: Proceedings on Privacy Enhancing Technologies.